## Slide 1: The sparse and low-rank interpretation of SVD-based denoising for vibration signals
Team 15 (AIE-C):
Arepalle Charan Kumar Reddy(24207)
Manda Rohit vardhan (24231)
Pagala Sai Vandith Reddy (24239)
Sirigiri Saradhi (24265)
22MAT230 Mathematics for Computing 4

## Slide 2: Problem Statement
Vibration signals acquired from rotating machinery are typically contaminated by strong background noise, making condition monitoring and fault diagnosis difficult.
Existing SVD methods can enhance fault-related components but often lead to amplitude distortion and inconsistent denoising performance.
Early-stage bearing faults generate weak impulsive components in vibration signals that are masked by noise and cannot be extracted using raw time-domain or frequency-domain analysis.

## Slide 3: OBJECTIVES
To model vibration signal denoising as a sparse and low-rank optimization problem using a matrix representation of time-series data.
To analyze and compare classical TSVD, heuristic reweighted SVD (RSVD), and weighted soft-threshold SVD (WSSVD)
To implement fault classification using machine learning models trained on features extracted from WSSVD-denoised signals.
To denoise acoustic signals (.wav/mp3), validating its robustness beyond vibration-only data.

## Slide 4: Methodology
1. Signal Acquisition
  Raw vibration signal is acquired from a bearing fault dataset (IMS) and modeled as:
Where:
( )
→ Fault features which we need to extract ()
e → Discrete frequency interference and background noise ()
m → length of the measured signal
2. Matrix Construction Using Hankel Representation The one-dimensional vibration signal is transformed into a structured Hankel matrix by extracting overlapping signal segments, enabling the preservation of periodic fault-induced impulsive characteristics.
patch from the time series
Length of each patch, n number of total patches, Overlap=l − 1

## Slide 5
3. Singular Value Decomposition (SVD) Singular Value Decomposition is applied to the constructed Hankel matrix to decompose it into orthogonal rank-one subspaces.
Where:
U left singular matrix whose columns are set as ( U ∈
diagonal matrix whose diagonal elements are set as the singular value ( ∈ )
)
singular value series is decreasing, ≥ ≥ ...
4. Optimization-Based Singular Value Processing
SVD-based denoising is formulated as a sparse and low-rank optimization problem.
We assume that the clean matrix X lies in the same singular vector subspace as Y, but with modified singular values:
Where X is an approximation of the desired matrix Y and are unknown coefficients to be estimated

## Slide 6
Representing as dictionary
Let
So
Let formulate as an optimization problem
Where:
is the Frobenius norm
λ is the trade-off parameter,
P(α) is the regularization of α.
and

## Slide 7
CASE 1: TSVD (ℓ₀ NORM)
So

## Slide 10
Case 2 : Proposed WSSVD ( weighted ℓ₁-norm minimization )
Standard ℓ₁ regularization treats all singular values equally and leads to uniform soft thresholding. This causes fault-related components to be penalized in the same manner as noise. To address this limitation, fault-related information is introduced through component dependent weights.

## Slide 13
5. Signal Reconstruction

## Slide 14: Results
Raw vibration signal acquired from the IMS bearing dataset, sampled at 20 kHz. The signal is heavily contaminated by noise, making early-stage fault-related impulses difficult to observe directly.

## Slide 15
Preprocessed vibration signal after DC removal, normalization, and segmentation to one second
Hankel matrix constructed from the vibration signal using overlapping patches (overlap = l − 1), preserving temporal correlation and enabling low-rank analysis.

## Slide 16
Singular value distribution of the constructed Hankel matrix
Time-domain comparison of denoising methods. WSSVD preserves impulsive fault characteristics more clearly than TSVD and RSVD.

## Slide 17
Thank you